## Slide 1: Numerical Problems on STATIC CHARACTERISTICS OF MEASURING INSTRUMENTS

## Slide 2: NUMERICALS
[1] A meter reads 115.50 V and the true value of the voltage is 115.44 V. Determine the static error, and the static correction for this instrument.
Solution:
The error is: Es = Am - At = 115.50 - 115.44 = +0.06 V
Static correction: δC = At - Am = -0.06 V.
[2] A thermometer reads 71.5oC and the static correction given is +0.5oC. Determine the true value of the temperature.
Solution:
True value of the temperature
At = Am + δC = 71.5+ 0.5 = 72.0oC

## Slide 3: NUMERICALS
[3] A thermometer is calibrated for the range of 100oC to 150oC. The accuracy is specified within 0.25%. What is the maximum static error?
Solution:
Span of thermometer = 150 - 100 = 50oC
Maximum static error = (0.2550oC)/100 = 0.125oC

## Slide 4: NUMERICALS
[4] An analogue indicating instrument with a scale range of 0 to 2.50 V shows a voltage of 1.46 V. A voltage has a true value of 1.5V. What are the values of absolute error and correction? Express the error as a fraction of the true value and the full scale deflection.
Solution:
Absolute error Es = Am - At = 1.46 - 1.50 = -0.04V
Absolute correction δC = δA = +0.04 V
Relative error Er = (Es /At)100 = (-0.04/ 1.50)100
= -2.66%
Relative error expressed as a percentage of full scale division = (-0.04/ 2.50)100 = -1.60%

## Slide 5: NUMERICALS
[5] A pressure indicator showed a reading as 22 bar on a scale range of 0-25 bar. If the true value was 21.4 bar, determine: i) Static error; ii)Static correction; iii)Relative static error
Solution:
i) Static error = 22 - 21.4 = + 0.6 bar
ii) Static correction = - (+0.6) = - 0.6 bar
iii) Relative error = 0.6 / 21.4 = 0.028 or 2.8 %

## Slide 6: NUMERICALS
[6] A pressure gauge which has a linear calibration curve has a radius of the scale line as 120 mm and pressure of 0 – 50Pa is displayed over an arc of 300o. Determine the sensitivity of the gauge as a ratio of scale length to pressure.
Solution:
300o = 300/180 = 5/3 radians
Full scale deflection = 5/3 radians
Length of full scale = 120mm5/3 = 200 mm
Sensitivity = 200/50 = 4 mm/Pa

## Slide 7: NUMERICALS
[7] A Wheatstone bridge requires a change of 7Ω in the unknown arm of the bridge to produce a change in deflection of 3mm of the galvanometer. Determine the sensitivity. Also determine the deflection factor.
Solution:
It may be noted that
i) A sensitive instrument can quickly detect a small change in measurement.
ii) Measuring instruments that have smaller scale parts are more sensitive.
iii)Sensitive instruments need not necessarily be accurate.

## Slide 8: NUMERICALS
[8] Determine the resolution of a voltmeter which has a range readout scale with 100 divisions and a full-scale reading of 100 V. If one tenth of a scale division can be read certainty, determine the resolution of the voltmeter.
Solution:
100 scale division = 100V
1 scale division = 100 /100 = 1V
Resolution = 1 x 1/10 = 0.1 V
[9] A transducer measures a range of 0-200 N force with a resolution of 0.20 percent of full scale. What is the smallest change in the force which can be measured by this transducer?
Solution: Range of force = 0-200 N
Resolution = 0.20 % of full scale
Smallest change in force which can be measured = 200 x 0.20 / 10= 0.4N